 Last New_Version PIR MP . ALARM
Function :
A,when the body is near,it will auto start the alarm;
B, The highest sensitivity in the range of 4-5 meters;
C, Put the alarm cat or paste in a certain height, away from the body within 5 meters within the angular range 120 ° left and right, as long as people or animals, swaying back and forth in a very short time, induction start.

D. Connectivity can listen to a location within 15 meters of the situation, the sound is very clear(when have no plugin the ear-set state).
using methods:
A) Power on: open the deck lid,insert the SIM card follow the instructions in Figure deck automatically boot.
B) Bind numbers Setting:
i):Communications tools such as mobile phone call connection after 15 seconds,Machine itself through to hear the voice call is binding,Operation is very simple,This way every time should be rebound.
ii): text "alm13800138000" sent to the machine,The "13800138000" is need to change the number, the binding After a successful machine return to SMS, in turn, change the number of backwardness to the machine, can bind mutil numbers, alarm when the machine will in turn make binding number all the time, the number no longer after answering the call, After binding number this way, I) binding number expire, And the number of binding boot do not need to bind again next time.
C) delete number :
Binding number for I) way, the card is automatically deleted, For ii) binding number, send "amov" delete all number,To end"amov13800138000"with"13800138000" to delete the specific number;
D) the query number :
Binding number for ii) way, send "achk" binding number query messages.
E) remote control configuration:
1) to send "SMS" to machine, the machine alarm mode to reply messages
2) send the "call" to machine, alarm mode switch to a normal phone call
3)Send "0000" to the SIM card number after a successful turn off this feature;
4) Send "1111" is open induction.

Frequency:
850MHZ, 900MHZ, 1800MHZ, 1900MHZ;

Standby time:
For body sensing:5-7days not for body sensing:15-20days.

Specification:
A, product size: 4.50*3. 0*1.40 cm
B, working current: below 10 mA
C, idle current ：below 0.05 mA
C, sensitivity: 5-8m center angle 90°